## Slide 1: NexusEdge: Leveraging IoT Gateways for a Decentralized Edge Computing Platform
Nabeel Nasir, Victor Ariel Leal Sobral, Li-Pang Huang, Bradford Campbell
University of Virginia
7th ACM/IEEE Symposium on Edge Computing (SEC), 2022

## Slide 2: A look back at last year’s SEC Keynote
Pete Beckman et al., “Harnessing the Computing Continuum for Programming Our World.” Fog Computing, 1st ed., Wiley, 2020
Raspberry Pi
4GB
WiFi
$40
Can we utilize
Gateways for
Edge Computing?

## Slide 3: Collecting Data from ~200 IoT Devices in Our Test Bed
Gateway 2
Gateway 3
Gateway 4
Estimote Beacon
CO2 Sensor
Temperature Sensor
Door Contact Sensor
Occupancy Sensor
Light Level Sensor
Herald Beacon
Leviton Lighting Control
Power Monitor
Smart Socket
Gateway 1
Gateway 5
Notes: Decided to deploy multiple sensors
Deployed around 200 sensors
We used some raspberry pi 4s to collect data from these sensors
We did some measurements of the gateways

## Slide 4: Gateways are Necessary but Underutilized
  Gateways necessary to cover IoT devices
  Have underutilized computational power
Notes: Data for 30 days

## Slide 5: Maximize Utility of Gateways for EC before relying on Servers
Devices
Gateways
Edge Server
Cloud
Notes: Cloud
Support responsive edge applications and cutting edge IoT devices using a distributed network of IoT gateways without requiring edge servers.

## Slide 6: Gateways offer Some Advantages over Server Machines
Better deployment flexibility
Wireless radios to communicate with IoT devices (one hop from devices)
Substantially lower cost (servers are $1000+)
No need to streaming all data to a centralized point
Also, IoT gateways are becoming better performant
Notes: Reduce network traffic and application latency
Spatially large deployments already have multiple gateways for network coverage, and leveraging them increases their value without incurring additional hardware and installation costs

## Slide 7: What kind of Edge Applications can we run on these gateways?
Suitable for:
  Long running applications
  Operates on streaming data
  Low to Moderate storage
  Low to Moderate compute
Not suitable for:
  Compute-intensive
  High storage apps
Examples: Live Video Analytics, Augmented Reality

## Slide 8: Machine Learning at the Edge
Object Detection [2]
Elderly Fall Detection [1]
[1] Hsu et al. “Fallcare+: An iot surveillance system for fall detection”, IEEE International conference on applied system innovation (ICASI), 2017.
[2] S. Tuli et al. “Edgelens: Deep learning based object detection in integrated iot, fog and cloud computing environments”, IEEE ISCON, 2019.

## Slide 9: Large Scale Sensing and Actuating
Occupancy based Building Energy Forecasting [6]
Distributed Soil Moisture Control [5]
[5] D.A.Winkler et al. “Wisdom: watering intelligently at scale with distributed optimization and modeling,” ACM SenSys, 2019.
[6] Y. Tang et al. “Establishment of enhanced load modeling by correlating with occupancy information,” IEEE Transactions on Smart Grid, 2019.

## Slide 10: Inherently Distributed Applications
Distributed Firmware Update for IoT Devices [4]
BLE Pairing Handoff across IoT Gateways [3]
[3] S. R. Hussain et al. “Seamblue: Seamless bluetooth low energy connection migration for unmodified iot devices,” ACM EWSN, 2017.
[4] S. Choi et al. “Blockchain-based distributed firmware update architecture for iot devices,” IEEE Access, 2020.

## Slide 11: Building An Edge Platform on Gateways poses some Challenges
Scaling up with multiple gateways has configuration overhead
IoT devices use heterogeneous communication techniques
Application development on a distributed network is complex
Managing apps and devices without a central point is hard
Gateways are not as resilient as server machines
  Middleware on Gateways to collaborate and execute applications!

## Slide 12: Some related works exist, but have limitations
Theme | Paper | Limitations
Gateway Coordination | Ooi et al. [1] | - Cannot execute edge applications
 | Clemente et al. [2] | - Doesn’t handle device heterogeneity - Interfaces with devices & apps not defined
[1] Ooi et al. “A collaborative iot-gateway architecture for reliable and cost effective measurements,” IEEE Instrumentation & Measurement, 2019.
[2] Clemente et al. “Fog computing middleware for distributed cooperative data analytics”, IEEE Fog World Congress (FWC), 2017.
IoT Middleware | ThingsJS [3] | - Excludes low-power and harvesting devices - Overhead for obtaining device streams
 | Hive Middleware [4] | - Not resilient to failures - Data locality not considered in scheduling
[3] Gascon-Samson et al. “Thingsjs: Towards a flexible and self-adaptable middleware for dynamic and heterogeneous iot environments”, 4th Workshop on Middleware and Applications for the Internet of Things, 2017.
[4] Essameldin et al. “More than the sum of its things: Resource sharing across iots at the edge”, IEEE/ACM Symposium on Edge Computing (SEC), 2020.

## Slide 13: NexusEdge Middleware on Gateways to Handle Challenges
Middleware
Middleware
Middleware
Middleware
Gateway 1
Gateway 2
Gateway 3
Gateway 4
Application
&
Management
Layer
Platform
Layer
Hardware
Layer
Notes: These are the gateways we’ve deployed in the link lab

## Slide 14: Middleware on Gateways to Handle Challenges
Application
&
Management
Layer
Platform
Layer
Hardware
Layer
Gateway discovery for scalability
Supports IoT device handling
Encapsulates current network
Notes: discovery - why BLE, why not some other?

## Slide 15: Using a Link Graph to Encapsulate Network Information
IoT environments are dynamic: devices and gateways could join and leave
For gateways to coordinate, each gateway needs to know:
  What other gateways are present
  What other devices are present
  Which gateways can communicate with which devices
Generating link graph: Ask neighbors, they ask their neighbors,…

## Slide 16: Challenging to Develop Apps when Devices are Distributed
NexusEdge Gives Developers an Abstracted Single Gateway View
Gateway 1
Gateway 2
Gateway 3
Gateway 4
temp4
lightcontrol1
lightcontrol2
lightcontrol3
temp1
temp3
temp2
Gateway

## Slide 17: APIs to Provide Simplicity in Device Interaction
temp4
lightcontrol1
lightcontrol2
lightcontrol3
temp1
temp3
temp2
Gateway
Receive data streams from temp4
Receive data streams from all temperature sensors
Turn on lightcontrol2 by sending a control message

## Slide 18: Middleware on Gateways to Facilitate this Shift
Application
&
Management
Layer
Platform
Layer
Hardware
Layer
Gateway discovery for scalability
Supports IoT device handling
Encapsulates current network
Distributed services to handle devices, applications, and data streams
Device interaction API hides underlying network complexity from apps
Provides remote management

## Slide 19: NexusEdge uses Device Locality to Schedule Applications
Gateway 1
Gateway 2
Gateway 3
Gateway 4
lightcontrol1
lightcontrol2
temp1
temp3
Auxiliary
Device
Middleware
Middleware
Middleware
Middleware
App
temp1
temp2
temp3
Devices Needed
temp2
schedule
Device connection
Data stream flow
executor
gateway
provider
gateway
Notes: Also does load balancing

## Slide 20: Resiliency: Migrates App if Executor Gateway Fails
Gateway 1
Gateway 2
Gateway 3
Gateway 4
lightcontrol1
lightcontrol2
temp1
temp3
Auxiliary
Device
Middleware
Middleware
Middleware
Middleware
App
temp1
temp2
temp3
Devices Needed
temp2
Device connection
Data stream flow
executor
gateway
provider
gateway
executor
gateway

## Slide 21: Resiliency: Provide Alternative Streams (if possible) when Provider Fails
Gateway 1
Gateway 2
Gateway 3
Gateway 4
lightcontrol1
lightcontrol2
temp1
temp3
Auxiliary
Device
Middleware
Middleware
Middleware
Middleware
App
temp1
temp2
temp3
Devices Needed
temp2
Device connection
Data stream flow
executor
gateway
provider
gateway
provider
gateway

## Slide 22: NexusEdge is open-source, containerized and Kubernetes-friendly
Implementation is open source
  github.com/uva-linklab/nexusedge
Containerized with Docker
  Handles gateway heterogeneity and improves deployability
Can be orchestrated using K3S (Lightweight Kubernetes)
  DaemonSet to deploy middleware on all gateways
Notes: Gateway devices are heterogeneous and have different hard- ware or runtime environments with various subtle differences. To handle this heterogeneity, we containerize our middleware using Docker [63] to provide operating system-level virtualization. This vastly improves the ease of deployment, and abstracts out the hardware, OS, and runtime environment. The NexusEdge Docker container is public on Docker Hub [64].
Additionally, to reduce the tedious burden of deployment on many gateways, we utilize K3S [65], a lightweight version of Kubernetes [66] container orchestrator built for IoT and Edge Computing. Gateways join a cluster, and the cluster executes a DaemonSet [67] to start the NexusEdge container on all cluster nodes. DaemonSet ensures that NexusEdge starts automatically on all new gateways

## Slide 23: Scalability with Devices and Applications
Comparison of decentralized NexusEdge vs a centralized server-based architecture
Decentralized NexusEdge Architecture
Centralized Edge Server Architecture

## Slide 24: Scalability with No. of IoT Devices
Setup
  Edge Server: 4 Raspberry Pis as Gateways, 1 Raspberry Pi as Server
  NexusEdge: 5 Raspberry Pis as Gateway, no Server
Measure:
  CPU usage
  Memory usage
  Network traffic

## Slide 25: Comparison with Centralized Architecture
Sensor | Data Rate | Count
Temperature Sensor | 100 bytes / 5 mins | 50
Occupancy Sensor | 100 bytes / 5 mins | 50
CO2 Sensor | 100 bytes / 15 mins | 10
Smart Meter | 500 bytes/s | 10
Camera | 100 KB/s (assuming 720p at 15fps) | 5
 |  | 125 (total)
Devices Simulated for the evaluation:
125 devices equally distributed on server and gateways, i.e. each hosting 25 devices
a) Scalability with No. of IoT Devices

## Slide 26: Scales well with more IoT devices
NexusEdge has substantially lower network traffic
  NexusEdge gateways only stream data when applications require it
Resource usages slightly higher for Edge Server architecture to handle data flooding
NW
Traffic
(KB/s)
No. of Devices
Avg.
CPU
Usage
(%)
No. of Devices
No. of Devices
Avg.
RAM
Usage
(MB)
Network Traffic
CPU Usage
Memory Usage

## Slide 27: Scalability with No. of Edge Applications
Setup
  Edge Server: 4 Raspberry Pis as Gateways, 1 Raspberry Pi as Server
  NexusEdge: 5 Raspberry Pis as Gateway, no Server
Measure:
  CPU usage
  Memory usage
  Network traffic
  End-to-End Latency (from device to application)

## Slide 28: Scalability with No. of Edge Applications
Sensor | Data Rate | Count
Temperature Sensor | 100 bytes / 5 mins | 50
Occupancy Sensor | 100 bytes / 5 mins | 50
CO2 Sensor | 100 bytes / 15 mins | 10
Smart Meter | 500 bytes/s | 10
Camera | 100 KB/s (assuming 720p at 15fps) | 5
 |  | 125 (total)
Devices Simulated for the evaluation:
Notes: We simulated 10 smart meters at 500 bytes/s,
50 temperature sensors at 100 bytes every 5 min.,
50 occupancy sensors at 100 bytes every 5 min.,
10 CO2 sensors at 100 bytes every 15 min., and
5 IP cameras at 100 KB/s assuming 720p at 15 fps.

## Slide 29: Scalability with No. of Edge Applications
App | Sensors Used
Power meter anomaly detection | 10 Smart meters
Object detection in secure areas | 5 Cameras
User comfort monitor | 50 Temperature Sensors
Air quality monitoring | 10 CO2 Sensors
Room scheduling | 50 Occupancy Sensors
Notes: 1) Power meter anomaly detection: Monitors power meter data from 10 smart meters, and sends an alert if it detects a spike in the power profile.
2) Object detection in secure areas of building: Obtains the camera feed from five IP cameras, extracts images from them, and uses a machine learning model trained on the ImageNet dataset, to check for any suspicious objects.
3) User comfort monitor: Collects data from the 50 temperature sensors from different office rooms and open areas, monitors for overheating or overcooling, and sends alerts to facilities.
4) Air quality monitoring: Periodically checks readings from ten CO2 sensors and alerts if certain areas cross dangerous ppm levels.
5) Room scheduling: Collects information from all occupancy sensors from the building floor to display available conference rooms.

## Slide 30: b) Scalability with No. of Edge Applications
Three different device distributions
  Colocated: Devices required for app available on executing gateway/server
  Distributed: Devices required for app equally distributed on all five nodes
  Random: Devices randomly distributed on all five nodes
Notes: “As the resource usage, traffic, and latency differ based on how devices are distributed, we consider three different types of device distributions”

## Slide 31: b) Scalability with No. of Edge Applications
Memory usage of ES is ~90% higher than NexusEdge, across distributions
  Reason: Single edge server to execute applications
CPU and memory usages in NexusEdge are very low, < 3% and 250 MB (out of 4GB) with 5 apps
  Shows potential to run edge applications

## Slide 32: Scales well with more edge applications
Centralized architecture suffers from high network traffic
  NexusEdge utilizes locality of data while scheduling applications
NexusEdge offers substantially better application latency (except for the distributed case)
Notes: For distributed case, applications end up needing data from all gateways, effectively performing similar to the centralized ES arch

## Slide 33: Comparison with AWS IoT Greengrass
We compare against Amazon’s AWS IoT Greengrass
Edge Computing platform that follows a Centralized architecture
Evaluation Setup
  Use 70 sensors from our testbed: temperature and occupancy
  App: Send alert for suboptimal cooling and wasted energy
Run application and measure network traffic and end-to-end latency
Notes: To validate our findings from previous study

## Slide 34: Improved Traffic and Latency Compared to Greengrass
Mean Traffic: 3.46 KB/s vs 8.48 KB/s
(2.5x lower)
Mean Latency: 13.83 ms vs 142.74 ms
(10x faster)
Notes: CDF for the network traffic and the latency it takes for a simulated sensor to create a data and to the application to actually use the data
Example for ultra low latency app: human perception on AR, app which operates by correlating events (timing is critical)

## Slide 35: Decentralization Overhead
Gateways have some decentralization overhead for gateway coordination
For servers, no scheduling is needed
Deploy an app and measure deployment time on server vs gateways
Notes: For server, no scheduling needed
For NexusEdge, send application to scheduling gateway, generating link graph, scheduling the application, dispatching the application to an executing gateway, setting up streams from provider gateways, and subscribing to all data streams

## Slide 36: NexusEdge has reasonable Decentralization Overhead
Deployment time of NexusEdge is 1110.4ms compared to 690.1ms for centralized
Overhead: 420ms
Notes: decentralization overhead - is this overhead okay?
- Okay since we deal with only long running app deployments

## Slide 37: Resiliency to Gateways Failures
Measure resiliency response time to failures
NexusEdge provides resilience for:
  Executor Failure: If a gateway executing an app fails, it’s migrated to a different gateway
  Provider Failure: If a gateway providing data streams to an app fails, the middleware tries to reinstate data streams from alternative sources

## Slide 38: NexusEdge Quickly Migrates Apps when Gateways Fail
Fail the executor gateway and measure migration time
Migrating an app using 100 data streams takes ~1.2s
Migration time increases linearly

## Slide 39: NexusEdge Quickly Reinstates Streams
Measure response time to reinstate stream from a failover gateway
Fast recovery: 712.3ms even with 5 gateways, 100 devices
Notes: Both experiments highlight significance of our middleware in building a cohesive edge platform with gateways, that can operate with resiliency without suffering from a single point of failure

## Slide 40: Case Study: Distributed Federated ML
Implemented a distributed federated machine learning without cloud support
Uses several distributed APIs provided by the middleware

## Slide 41: Limitations and Future Work
Currently offers limited security provisions
  Interfaces for device registration, discovery, and auxiliary devices could be updated
Task scheduler to improve QoS of edge apps by utilizing heterogeneity of edge hardware
Device stream routing for user-driven privacy policy enforcement
Notes: Security Challenges: Security is a major consideration for edge computing systems. We use a limited threat model in this work with preliminary security provisions. To enhance security, we need to explore different threat models for the platform, apps, devices, auxiliary devices, and data. Certain interfaces including device registration, gateway discovery, and auxiliary device connections, could support security features.

## Slide 42: Takeaways
IoT Gateways are ubiquitous and becoming increasingly performant
Increase their utility in the computing continuum before depending on more powerful machines
NexusEdge middleware a first step towards a vision to democratize edge computing
Notes: Make edge computing accessible to all

## Slide 43: Thank You!
I’m on the job market!
Nabeel Nasir
www.cs.virginia.edu/~nn5rh