## Slide 1: Untangling the Cloud from Edge Computing for IoT
Nabeel Nasir
Advised by: Prof. Bradford Campbell

## Slide 2
By 2025
55 Billion IoT Devices
73 Zettabytes of Data
Source: International Data Corporation (IDC)

## Slide 3: Edge Computing to Handle Massive Influx of IoT Data
Devices
Gateways
Edge Server
Cloud
Notes: ec is one solution which prescribes a tiered architecture
you have devices at the bottom most layer
you have gateways - devices like raspberry pis - which has wireless radios to communicate with devices
the central piece is an edge server within your local network, which runs applications, without depending on the cloud
but the cloud is used as the control plane for orchestration and configuration

## Slide 4: Cloud and Edge Server Dependence an Obstacle
“Off-grid” usage
Cloud and bandwidth costs
Scalability
Access to a server
Limited Privacy Controls
Devices
Gateways
Edge Server
Cloud
Notes: there are some issues with this architecture
relying on the cloud is impractical in some use cases where there is no internet connection, like a remote deployment with no access, or in a secure deployment like a hospital where cloud access is not preferred
there are some cloud and bandwidth costs involved
requiring prior configuration at the cloud hinders scalability
another key assumption is that every deployment will have access to an edge server, which is extremely unrealistic for most use cases
also all data from a deployment is usually treated as owned by a single entity, with no transparency or privacy control for individuals

## Slide 5: Leverage Gateways for Edge Computing
Gateways indispensable for IoT
Increasingly capable
Relatively Inexpensive
Devices
Gateways
Edge Server
Cloud
Notes:   Leverage Gateways for Edge Computing
  Focus on the gateways
  Show the two points
  First point to enforce privacy

## Slide 6: Key Ideas to Remedy Cloud & Edge Server Issues
Distributed Gateway Network instead of an Edge Server

## Slide 7: Distributed Gateway Network Instead of Edge Server
Devices
Gateways
Edge Server
Cloud
Notes: Cloud
Support responsive edge applications and cutting edge IoT devices using a distributed network of IoT gateways without requiring edge servers.
Comparison figure (with the server vs with the distributed gateways)

## Slide 8: Shifting From an Edge Server Poses Some Challenges
Overheads with Decentralization
  Easier application code with simple centralized model
  No central point to manage platform
Scalability
  Gateway configuration could pose overhead in scaling
Resource Constraints
  Limited resources like storage, GPUs etc.
Resilience
  Gateways not as sturdy as a server machine

## Slide 9: Middleware on Gateways to Facilitate this Shift
Application
&
Management
Layer
Platform
Layer
Hardware
Layer
Gateway discovery for scalability
Supports IoT device handling
Encapsulates network topology
Distributed services to handle devices, applications, and data streams
Device interaction API hides underlying network complexity from apps
Provides remote management
Notes: Briefly touch on lightweight containerization, and distributed storage

## Slide 10: Key Ideas to Remedy Cloud & Edge Server Issues
Distributed Gateway Network instead of an Edge Server
Specialized Edge Hardware for Elasticity

## Slide 11: Edge Gateways Becoming Increasingly Capable and Specialized
Raspberry Pi
Google Coral
with Edge TPU
NVIDIA Jetson
Xavier NX
Substantially cheaper
Can match app requirements
Directly interact with IoT devices
Better deployment flexibility
Notes: https://developer.nvidia.com/embedded/jetson-xavier-nx-devkit
https://www.raspberrypi.com/products/raspberry-pi-4-model-b/
https://coral.ai/products/dev-board
Substantially cheaper than edge servers
Specialized hardware can match application requirements
Low-power wireless radios to interact directly with IoT devices
Increased deployment flexibility compared to servers

## Slide 12: Utilize Specialized Edge Hardware for Elasticity
Scale out by adding a new gateway
Devices
Gateways
Schedule based on requirements
Notes: Start small and add new hardware if needed to Scale out
- Use a distributed task scheduler to match application requirements with gateways capabilities to provide best available quality of service to applications.

## Slide 13: Scheduler uses Requirements, Capabilities and Resource Usages

## Slide 14: Scheduling the Key Challenge, and Different from Other Domains
Optimal scheduling algorithm based on
  Application requirements
  Gateway capabilities
  Gateway resource usages
Different from Task Schedulers in other domains:
  Grid Computing, Cluster Computing: Mostly homogeneous machines
  Real-time scheduling: Requires execution times and deadlines
  Function-as-a-Service Platforms: App’s requirements or machine’s capabilities not considered
Notes: Add table

## Slide 15: Key Ideas to Remedy Cloud & Edge Server Issues
Distributed Gateway Network instead of an Edge Server
Specialized Edge Hardware for Elasticity
Privacy Policies enforced on Gateways to empower Users

## Slide 16: People in Shared Spaces have No Idea About Their Sensed Data
Notes: In shared spaces, users have no idea about what's being sensed or which applications are using their data.
Empower users in shared spaces with collaborative privacy policies that operate closest to the devices to provide more transparency and better control of their data.

## Slide 17: Utilize Existing Sensor Stream Service to Enforce Policies
Stream Manager
Middleware
Stream Manager
Middleware
Stream Manager
Middleware
T1
T2
App
Policy: Don’t share T1 with App

## Slide 18
Stream Manager
Middleware
Stream Manager
Middleware
Stream Manager
Middleware
T1
T2
App
Gateway 1
Gateway 3
Gateway 2

## Slide 19: User-driven Privacy Policies to Empower People
Users can specify policies like:
  Allow access to occupancy data to all apps, but only from 9AM – 5PM
  Share occupancy data to an emergency evacuation app, but not to room scheduling app
Challenge:
  Simple user interface to convey this complex information
Novelty:
  Some privacy policy works exist, but novel way of policy enforcement

## Slide 20: Conclusion
Democratize Edge Computing by untangling it from cloud and edge server dependencies
Utilize inexpensive gateway network to execute applications
Empower users by providing transparency and control over data

## Slide 21: Thank you!
Questions?
You can find me on:
  Website: http://www.virginia.edu/~nn5rh
  Email: nabeeln@virginia.edu
  LinkedIn: https://www.linkedin.com/in/nabeel-nasir/
I am seeking summer internship opportunities!